## Slide 1: iot.schema.org
Practical Semantic Interoperability for Connected Things
or - Avoiding the XKCD 927 Effect
Michael Koster

## Slide 2: This is mostly informational
What problem is being solved ?
What is iot.schema.org ?
How does iot.schema.org work ?
Who is iot.schema.org for ?
How is iot.schema.org intended to be used ?
What is the status, the gaps ?
How do I get involved ?

## Slide 3: This is the Problem being solved:
Source: https://xkcd.com/927/

## Slide 4: Background
IoTSI - IoT Semantic Interoperability Workshop
WISHI – Work on IoT Semantic and Hypermedia i15
Many different models and protocols for a common set of high level patterns
Semantic Normalization vs. Protocol Translation
Diversity in device protocols is a feature

## Slide 5: Problem being solved – Semantic Interoperability for IoT
Acknowledge the diversity of IoT device ecosystems
  Not another device standard
  Adaptive to diverse protocol, language, and data models
  Distill the common and stable operational features
  Second "narrow waist" for systems above IP networks
Address the ease of use of Semantic Web for IoT and use of IoT for Semantic Web
  Not another IoT ontology
  A conceptual layer that models connected things in relation to existing ontologies

## Slide 6: Narrow Waist in System Design
OCF
dotdot
LWM2M
Fairhair
IP Networks LAN/WAN (WiFi, Thread)
Semantic Interoperability (Software Adaptation)
App
App
App
App
Many Applications. Local and Remote
Many Devices, Different Ecosystems
Common Infrastructure
(Protocols, Formats, and Meta Models)
Internet of Things
Web of Things

## Slide 7: Diverse Devices and Applications, Common Protocols and Semantics
Transport
UDP/TCP
Protocols, Formats
IETF CoAP, CBOR, Link-Format
Device Ecosystems
OCF, OMA, Zigbee, Fairhair
Networks
WiFi, IPV6, Bluetooth
Protocol Binding
Thing Description
Semantic Vocab
W3C Thing Description
iot.schema.org
Internet of Things
Narrow Waist
of Protocols
Web of Things
Narrow Waist
of Semantics
Applications
Interoperable Applications
Diverse Applications
Diverse Devices

## Slide 8: What is iot.schema.org
A layer to bridge between device ecosystems and Semantic Web technology, consisting of
Publicly available, reusable, interoperable, and compose-able definitions for connected things
Property and relation types to enable reuse of existing ontologies and definitions
  SSN, SOSA, SAREF, QUDT
  Property types for e.g. Feature of Interest
Follow the example and align with Schema.org
  Extend the schema.org patterns
  Community contributions and open license

## Slide 9: iot.schema.org Definitions
Semantic definitions that follow the design patterns and interaction affordances of connected thongs
Interoperable due to a set of static and dynamic semantic constraints
Define a "Capability" that represents – typically – the smallest practical compose-able unit of functionality
For example, a temperature sensor, or a door lock

## Slide 10: iot.schema.org Capabilities
Abstract functionality around a simple functional concept, e.g. temperature sensor, or door lock
Often associated with a class of physical quantity or artifact, e.g. "temperature" or "door"
Capabilities are associated with Interactions and Data Items in the iot.schema.org conceptual model
The Interactions and Data Items are the basis for protocol and data-model neutral definitions

## Slide 11: iot.schema.org Categories/Classes
schema:thing
Capability
InteractionPattern
Action
Event
Property
acceptsInputData
providesOutputData
providesInteractionPattern
rdfs:subclassOf
schema:Property
iotschema Class
Reused Class
DataItem
schema:PropertyValue
schema:PropertyValueSpec.

## Slide 12: iot.schema.org Categories
Capability
  Discovery of things that satisfy application requirements
  Static constraints as part of the definition
Interaction
  Adaptation of the application to the affordances of the connected thing
  Static constraint with compose-able elements
Data Item
  Adaptation of the application to the data format, types, engineering units, range and scale
  Static or dynamic constraints

## Slide 13: iot.schema.org Conceptual Integration with other ontologies
Feature of Interest concepts and property types to describe location, equipment, or other classifiers
For example, BrickSchema definitions from Haystack
Quantity and Units constraints can use QUDT concepts and appropriate identifiers
SSN, SOSA, SAREF concepts can extend a definition
Definitions and instances may be annotated in RDF

## Slide 14: Integration with other Ontologies
iot.schema.org Definition
Feature of Interest, O&M Situation, Provenance
Quantities, Units, Shapes, Property Value Constraint
Software Affordances
Enables Well-Characterized interactions with Physical Entities

## Slide 15: Connect things to the real world
Door Lock
Door
DoorLock Capability
- ActuateLock Interaction
- ActuateUnlock Interaction
- GetState Interaction -> LockState Data
isAssociatedWith
- Is A Front Door
- Opens To Outside
- Is A Security Door
"Lock Security Doors and Check" Action
iot.schema.org
other ontologies

## Slide 16: Feature of Interest Properties

## Slide 17: iot.schema.org Specific Use Cases
Semantic annotation of thing and data instances
  RDF instances, LDP, etc.
  WoT Web of Things Thing Description
  HTML Web page using microformats or JSON-LD in <script> tag
  Target attributes in web links (RFC8288 et. al.)
  Metadata for ad-hoc annotation as type
Selective Semantic Discovery using YFQL
Automatic configuration of IoT applications, rules, and behaviors
Standalone semantics for data analysis, data at rest

## Slide 18: W3C WoT Thing Description
Semantic annotation for Thing Description instances
Describes Things using Capability identifiers
Describes TD Events, Actions, and Properties using Interaction identifiers
Describes DataSchema instances using Data Item identifiers and constraint systems
Thing Description contains concrete Protocol Bindings for specific transfer layer operations

## Slide 19: Extended use Cases are enabled
Declarative Semantic API using the meta-interaction model directly
Abstract constructor language for building and composing instances of exposed things
  OCF, OMA LWM2M/IPSO, Zigbee/dotdot, BLE
  C2C API management (OpenAPI + Semantic Annotation)
  HAL, Hydra, JSON-Hyperschema,..
Interoperable definitions for orchestrations: rules, behaviors, scenes, and enumerations

## Slide 20: Status
Monthly Teleconferences since mid-2017
Examples of Definitions in a Github repository
FoI annotation examples are also in the repo
Prototypes tested at W3C Web of Things Plugfests and WISHI/IETF Hackathons from mid 2017
Some contributors are ready to begin submittting definitions
We need to build out some tools and processes
W3C Community Group with Web of Things

## Slide 21: References
iot.schema.org
  https://github.com/iot-schema-collab/teleconferences/blob/master/README.md
  https://github.com/iot-schema-collab/intro-materials
  https://github.com/iot-schema-collab/teleconferences
W3C Web of Things IG/WG
  https://www.w3.org/WoT/WG/

## Slide 22: Thank You!
Questions ?